# MRD: Aegis Gardner (Project: "The Mule")
Version: 1.4 (Integrated Mechanical Protocols & Audio Reflex)
Status: Product Development Phase
## 1. Executive Summary
The Aegis Gardner platform, "The Mule," is an autonomous "Estate Assistant" designed for heavy-duty hauling and precision yard maintenance.
The architecture is modular and Intelligence-First. Key differentiators include centimeter-level navigation via a 915MHz RTK link, high-bandwidth WiFi backhaul via an ESP32 bridge, and a hard-wired safety layer that can override the AI Brain via direct sensor feedback.
Scale of Operation: Optimized for properties up to 2 acres , maintaining full load capacity on inclines up to 10%.
## 2. Phased Development & Feature Roadmap
Feature	Base Platform (V1)	Heavy-Duty Tier (V2)
Navigation	RTK-GNSS + 915MHz Link + SLAM (Named Locations)	RTK-GNSS + Optional VSLAM
Obstacle Detection	2D LiDAR (10" height) + Ultrasonics + 1080p Video	3D LiDAR + Vision Fusion
Connectivity	ESP32 WiFi (Backhaul) + 915MHz (Nav)	Unified Industrial Long-Range Mesh
Towing Capacity	250 lbs (Threshold)	500 lbs (Obj)
Utility	Zone Mowing, Hauling & "Follow-Me" (5ft fixed)	Robotic Arm / Multi-Tool Support

## 3. Detailed Technical Requirements
### 3.1 Connectivity & Infrastructure
- Primary Backhaul (ESP32 WiFi): Serves as the high-speed 2.4GHz link for system logs and compressed 1080p video telemetry.
- Navigation Sub-Link (915MHz): Dedicated long-range radio providing RTCM corrections directly to the ZED-F9R rover module.
### 3.2 Positioning: RTK-GNSS & "Perfect Edge"
- Requirement: Achieve 2.5cm horizontal precision for boundary edging and fine-motor tasks.
- Implementation: Dual-band RTK receiver.
- Location Memory: System must utilize SLAM to support named-location navigation, allowing users to command specific destinations (e.g., "Go to Shed," "Dock").
### 3.3 Power & Endurance
- Battery Endurance (Mowing): Minimum 4 hours continuous operation.
- Battery Endurance (Hauling): Minimum 2 hours continuous operation carrying 250 lbs on flat terrain.
- Audio Power Optimization: To preserve battery and reduce signal noise, the microphone array must automatically disable when high-draw motors (mowing blades) are active.
### 3.4 User Interface: Voice & Vision
- Voice Interface: Integrated multi-microphone array supporting wake-word activation and NLP for location-based commands.
- Follow-Me Feature: Uses the 1080p passive vision layer for human classification. The system will maintain a fixed following distance of 5 feet.
## 4. Hardware Architecture & Safety Authority
### 4.1 The Cognitive Layer (NVIDIA Jetson Orin Nano)
- Role: Handles high-level path planning, SLAM, and Vision AI processing.
- Constraint: Receives LiDAR and Nav data for path planning but has no authority to override the ESP32's safety state.
### 4.2 The Reflex Layer (ESP32 - Master Safety Controller)
- Requirement: The ESP32 serves as the master safety watchdog with direct physical authority over the motor controllers.
- Kill Switch Logic: The ESP32 triggers an immediate hardware shutdown (physical disconnect) if:
  - Any sensor reports a critical threshold violation.
  - The "Heartbeat" signal from the NVIDIA Jetson fails.
- Hardware Diagnostic Accessibility: The custom control PCB must include exposed test points for all primary power rails (24V, 19V, 5V, 3.3V) and critical safety signals (PWM Heartbeat, Relay Trigger, and Bumper State).
### 4.3 Multi-Modal Obstacle Detection
- 2D LiDAR: 360-degree horizontal scan at a fixed height of 10 inches.
- Ultrasonic Array: 3-5 sensors for near-field collision avoidance ($<20$cm).
- Vision Layer: 1080p passive sensor.
## 5. Mechanical Architecture & Assembly Protocols
Strict adherence to these protocols is required to prevent structural fatigue.
### 5.1 Main Chassis Construction
- Material: 1" square steel tubing (11ga / 0.120" wall thickness).
- Load Capacity: Chassis must support a static/dynamic load of 250 lbs.
- Assembly Protocol (Mandatory):
  - Hardware: M8 x 1.25 Grade 8.8 (Zinc Plated) with Nyloc nuts.
  - Torque Spec: 24 Nm (~18 lb-ft).
  - CRITICAL CONSTRAINT: Crush Sleeves Required. You cannot bolt directly through the 1" tubing. A metal crush sleeve must be inserted at every bolt point to prevent tube deformation and subsequent loosening due to vibration.
### 5.2 Mower Deck Interface (Kobalt 16-inch Poly Deck)
- Coupling Architecture: 3-Point Parallel Linkage.
- Logic: The mower deck must "float" vertically independent of the chassis. Rigid mounting is forbidden to prevent traction loss or ground scalping.
- Linkage Mechanism:
  - Custom laser-cut 3/16" aluminum adapter plates bolted to handle-pivot lugs.
  - Connected via two lower drag links and one upper adjustable turnbuckle.
- Assembly Protocol:
  - Hardware: M6 x 1.0 Grade 8.8 bolts.
  - Torque Spec: 10 Nm.
  - CRITICAL CONSTRAINT: Fender Washers Required. Large-diameter fender washers must be used on the underside of the polymer deck to distribute clamping load and prevent bolt pull-through.